## Slide 1: SOBEL FILTER IMPLEMENTATION AND OPTIMIZATION: A COMPARATIVE SOFTWARE AND HARDWARE APPROACH
Professor: Bellas Nikos
Students: Vasileiou Christos, PID: 1983
Voulgaris Dimitris, PID: 2052
Department of Electrical and Computer Engineering
University of Thessaly, Greece
CE435: Embedded Systems Course
Spring 2019

## Slide 2: Software Implementation Optimizations (1)
  Compiler optimizations (-O3)
  Loop Unrolling
    In function“Convolution2D”
  Loop Interchange
    Exploit 32KB cache of Cortex-A9 by computing elements row-by-row
  Function Inlining
    Get rid of function “Convolution2D”
24-Jun-19
ECE - University of Thessaly

## Slide 3: Software Implementation Optimizations (2)
  Strength reduction
    Get rid of “math.h” functions
    Replace them with mathematic operations
  Common Sub-expression Elimination
    In function“Convolution2D”
  Algorithm Specific Optimizations
    Get rid of filter kernels
    Replace them with in lined math operations
24-Jun-19
ECE - University of Thessaly

## Slide 4: Software Implementation Optimizations (3)
  The previous kept a stable, infinite PSNR.
  Further performance improvement is possible at the expense of PSNR, i.e. image quality
  Visually there is no difference
  Manhattan Distance Optimization
    becomes
24-Jun-19
ECE - University of Thessaly

## Slide 5: Software Implementation Results (1)
25-Jun-19
ECE - University of Thessaly
Chart: Total Execution Time
| -O0 | -O3 | loop unroll | loop interchange | algorithm opt | print variables | nosqroot | <<1
 | 1.6805 | 0.08786 | 0.087782 | 0.078192 | 0.057288 | 0.049798 | 0.019556 | 0.017194
Chart: Total Execution Time (zoom in)
| -O3 | loop unroll | loop interchange | algorithm opt | print variables | nosqroot | <<1
 | 0.08786 | 0.087782 | 0.078192 | 0.057288 | 0.049798 | 0.019556 | 0.017194
Overall Time Reduction: ~99% (from –O0 @ 1.68 sec to final @ 0.0172)
Partial Time Reduction: ~80% (from –O3 @ 0.088 sec to final @ 0.0172)

## Slide 6: Software Implementation Results (2)
24-Jun-19
ECE - University of Thessaly
Chart: Execution Time Reduction from Previous Optimization (%)
| -O3 | loop unroll | loop interchange | algorithm opt | print variables | nosqroot | <<1
 | 94.7717 | 0.088778 | 10.9242 | 26.7347 | 13.0743 | 60.7293 | 12.0781
Chart: Standard Deviation
| -O0 | -O3 | loop unroll | loop interchange | algorithm opt | print variables | nosqroot | <<1
std. Deviation | 0.0044114 | 1.101e-05 | 8.2098e-06 | 2.4413e-06 | 1.4142e-06 | 4.0012e-06 | 2.2383e-06 | 2.1909e-06
Chart: Standard Deviation
| -O3 | loop unroll | loop interchange | algorithm opt | print variables | nosqroot | <<1
std. Deviation | 1.101e-05 | 8.2098e-06 | 2.4413e-06 | 1.4142e-06 | 4.0012e-06 | 2.2383e-06 | 2.1909e-06

## Slide 7: Hardware Implementation The IP Creation (1)
  Transfer optimized C/C++ code in Vivado HLS
  BUT
  Data size is too big to fit in FPGA memory
  Decide the data transfer method:
  stream
  burst mode
    Use “memcpy” to enable fast data transfer
24-Jun-19
ECE - University of Thessaly

## Slide 8: Hardware Implementation The IP Creation (2)
  How many elements are to be transferred each time?
  Try-and-error
  Compute output image in tiles (ROWS x COLS) of :
    130x1024
    66x1024
    34x1024
    18x1024
  Opt for 130x1024 because of:
    Better overall performance (will explain later)
    More resource utilization (will explain later)
24-Jun-19
ECE - University of Thessaly

## Slide 9
0
1
2
3
…
126
127
128
129
0 1 2 3
1022
1023
1021
INPUT ARRAY
Christos Vasileiou
Dimitrios Voulgaris
25-Jun-19
ECE - University of Thessaly
Hardware Implementation The Algorithm (1)

## Slide 10
Blocks are segments of initial image.
Each block is loaded in FPGA’s memory (BRAMs).
Each block is responsible for feeding the sobel filter.
Size is 130*1024 bytes
Input Image
IBlock0
IBlock1
IBlock7
…
Christos Vasileiou
Dimitrios Voulgaris
25-Jun-19
ECE - University of Thessaly
Hardware Implementation The Algorithm (2)

## Slide 11
IBlock0
IBlock1
IBlock7
…
1. Blocks are segments of initial image.
2. Each block is loaded in FPGA’s memory (BRAMs).
3. Each block is responsible for feeding the sobel filter.
4. Size is 130*1024 bytes.
Input Image
Christos Vasileiou
Dimitrios Voulgaris
25-Jun-19
ECE - University of Thessaly
Hardware Implementation The Algorithm (2)

## Slide 12
IBlock0
IBlock1
IBlock7
…
Sobel filter processes each input block to extract an output block
Output blocks size is reduced by 1 row.
OBlock0
OBlock1
OBlock7
…
0
..
129
0
..
129
0
..
129
0
..
128
0
..
128
0
..
128
Christos Vasileiou
Dimitrios Voulgaris
25-Jun-19
ECE - University of Thessaly
Hardware Implementation The Algorithm (3)

## Slide 13
IBlock0
0
..
129
1. Blocks are segments of initial image.
2. Each block is loaded in FPGA’s memory (BRAMs).
…
…
IBlock1
0
..
129
IBlock7
0
..
129
Output Image
Christos Vasileiou
Dimitrios Voulgaris
25-Jun-19
ECE - University of Thessaly
Hardware Implementation The Algorithm (4)

## Slide 14
OUTPUT ARRAY
Columns 0 and 1023 are always initialized with zeros.
For the first and last output segment the rows 0 and 128 are initialized with zeros.
Christos Vasileiou
Dimitrios Voulgaris
25-Jun-19
ECE - University of Thessaly
0 1 2 3
0
1
2
3
…
126
127
128
129
1022
1023
1021
Hardware Implementation The Algorithm (5)

## Slide 15: Hardware Implementation The Block Diagram (1)
25-Jun-19
ECE - University of Thessaly
  Zynq7 Processing System
  Sobel IP
  AXI Interconnect (x2)
  Processor System Reset (by default)
  Use AXI-Lite protocol with 3 communication channels:
    1st to control IP operation
    2nd to fetch input image segments
    3rd to export output image segments

## Slide 16: Hardware Implementation The Block Diagram (2)
25-Jun-19
ECE - University of Thessaly

## Slide 17: Hardware Implementation Optimizations (1)
25-Jun-19
ECE - University of Thessaly
  The main Sobel code consists of 3 loops:
    BLOCK_LOOP
    OUTER_LOOP
    INNER_LOOP
  We experimented with:
    Different combinations of “loop unrolling” and “loop pipelining”
    Different array sizes that affect all loop iterations
    Array partitioning for parallel execution
    Frequency modification

## Slide 18: Hardware Implementation Optimizations (2)
25-Jun-19
ECE - University of Thessaly
  Final optimizations:
  Unroll BLOCK_LOOP by factor of 2
  Pipeline INNER_LOOP
  Unroll “zero-setting” loop complete

## Slide 19: Hardware Implementation Optimizations (3)
25-Jun-19
ECE - University of Thessaly
Summary |  |  |  |  |  |  |  |  |  |  |  | 
Timing Summary | target | 10 | 10 | 10 | 10 | 10 | 10 | 8 | 7 | 6 | 5.5 | 7.3
 | estimated | 8.62 | 8.75 | 8.75 | 8.75 | 8.75 | 8.75 | 7 | 6.12 | 5.38 | 5.38 | 7.24
 | uncertainty | 1.25 | 1.25 | 1.25 | 1.25 | 1.25 | 1.25 | 1 | 0.88 | 0.75 | 0.69 | 0.91
Latency | min | 64762177 | 50239641 | 6320297 | 6448297 | 6361681 | 6452217 | 6453241 | 6452729 | 6455873 | 6456897 | 6296725
 | max | 64762177 | 50264217 | 6357145 | 6485145 | 6443537 | 6493145 | 6494169 | 6493657 | 6496801 | 6497825 | 6317189
 | avg | 64762177 | 50251929 | 6338721 | 6466721 | 6402609 | 6472681 | 6473705 | 6473193 | 6476337 | 6477361 | 6306957
Utilization (%) | BRAM | 0 | 92 | 92 | 92 | 24 | 12 | 12 | 12 | 12 | 12 | 92
 | DSP | 35 | 0 | 0 | 14 | 1 | 0 | 0 | 0 | 0 | 0 | 0
 | FF | 9 | 5 | 6 | 27 | 8 | 13 | 13 | 20 | 22 | 23 | 5
 | LUT | 22 | 11 | 26 | 42 | 29 | 30 | 30 | 38 | 39 | 39 | 21
Trip Count: |  | 1022 | 8 | 8 | 8 | 16 | 8 |  | 8 |  | 8 | 4
Info: | INNER |  |  | pipeline | Pipeline + unroll 16 | Pipeline | Pipeline | Pipeline | Pipeline | Pipeline | Pipeline | Pipeline
 | OUTER |  |  |  |  |  |  |  |  |  |  | 
 | BLOCK |  |  |  | no unroll | Unroll 2 | Unroll 8 | Unroll 8 | Unroll 8 | Unroll 8 | Unroll 8 | Unroll 2
 | ARRAY_ROWS |  |  | 130 | 130 | 34 | 18 | 18 | 18 | 18 | 18 | 130

## Slide 20: Hardware Implementation Optimizations (4)
25-Jun-19
ECE - University of Thessaly
Chart: Total Execution Time In Hardware
| simple | memcpy | 8loops | 32loops | 8p-64loops-manhattan | 7.3p_8loops-manhattan
 | 0.25129 | 0.25131 | 0.031752 | 0.032127 | 0.025942 | 0.017306
Overall Time Reduction: ~93% (from 0.25sec to final @ 0.0173)

## Slide 21: Hardware Implementation C/C++ Code (2)
25-Jun-19
ECE - University of Thessaly
  Configure timer
  Disable interrupts
  Prepare input/output files
  Start timer
  Call Sobel HW accelerator
  Stop timer
  Compute PSNR
  Write output

## Slide 22: Thank You
25-Jun-19
ECE - University of Thessaly